## Slide 1: Project: Electrification of Haiti (Solar Aspect)
Benefits:
HEALTH: Indirectly could be beneficial to health due to education for adults.
SUSTAINABILITY: Moderate –Shouldn’t be high maintenance, but maintenance is not easy for locals and could be expensive.
COST: None for them
HAITIAN OWNERSHIP: Low, but they could install it, and it could be used as a teaching about energy.
Image from Project
Background: The Peltan Christian School in Haiti would like to have a zero-cost source of electricity in order to power lights in their building at night to have adult vocational classes. One of the options being considered for this is solar panels mounted on the school’s roof.
Objectives:
Zero cost for Haitians
Provides enough electricity to power lights that give enough light for reading
Infrequent maintenance
Findings/Solutions:
Buying Solar Panels is an option
Building Solar Panels is another option
Their power needs are feasible at a reasonable cost.
  360 W * 4 hr = 1440 Wh/day (for half the building)
  8 hours of sun = 180 W panels will do
Negatives:
Maintenance costs may be high
Difficult to find Haitian ownership aspect

## Slide 2: Electricity Needs
30 foot-candles is the standard here for reading. However, that is probably relatively bright, so estimates were done with 20 fc.
School is about 23 by 47 feet internally.
If we light half, 11 * 23 feet = 253 square feet.
Simple Lumen Method:
  Fc = total lumens/ (2 * Area) , total lumens = Fc*2*Area
  Total Lumens Needed = about 10,120
  800 lumens per bulb = 12 to 13 bulbs
  About 15 watts per bulb (CFL) = 360 Watts
  360 W * 4 hrs/day = 1440 Watt-hours per day

## Slide 3: Solar Options
Buy pre-made panels
  8 hours of sun/day (4 hours of power needed, so half the Watts needed)
  About $3 per Watt (high estimate)
  360 Watts / 2 = 180 W, 180 W * $3/W = $540
Make Our own
  At http://www.mdpub.com/SolarPanel/ directions are given for how one man built a 60 W panel for about $100. If we estimate $150/ 60 W, that’s $450, but a lot of work. 

## Slide 4: Homemade Solar Panel Building Process
Base for Panel
Completed Panel
Soldering Cells Together
Panel in Use
Charge Controller

## Slide 5: What else we will need:
One Inverter $150
One Charge Controller (May be able to build one) $150
Twelve Bulbs (CFLs) $60
Wiring $50
Light Fixtures $50
Two deep-cycle Lead-Acid batteries $100
(Very) Rough Cost Estimate: $560
(Plus Misc. Hardware and Solar Panels)